## Slide 1
Radiation Energy Deposition on an Asteroid
2d Lt Ashwin Rao
Air Force Institute of Technology
6 December, 2018

## Slide 2: Overview
Problem
Project Goals
  Key concept
Previous Work
MCNP Model
Results
Conclusions
Notes: Goals, Lit, Exp, Model, optimize, results, conc.

## Slide 3: Problem
Asteroid impact on earth could be catastrophic[9]
Potential solution: use a nuke[5]
  Detonate some distance away from surface
  Fragment, ”blow-off” enough material to change path
Dependent on energy deposited from detonation[1]
  Radiation interactions with asteroid (scattering, absorption)
  What yield and detonation distance?
Analyze energy deposition from different radiation
Notes: Goals, Lit, Exp, Model, optimize, results, conc.

## Slide 4: Project Goals
Create an MCNP model of an asteroid and use MCNP to characterize energy deposition from different types of radiation
Calculate total energy deposition, develop depth profile
Modify SDEF card with built in 14.1 MeV source to analyze effects of different particles/energies
  Use Watt spectrum
Notes: Model
Automated Opitmizaiton
ADVANTG adjoint Flux calc

## Slide 5: Previous Work
MAJ Ferguson’s thesis. [1]
Calculated neutron yield efficiency (function of Edep) for 2.45, 14.1 MeV neutrons, and thermonuclear spectrum.
Tested 8 different asteroid compositions.
Used MCNP input files as a base for testing different radiation
  Allende meteorite [2][4] and ice compositions
Notes: Manufacturer issues
10-0.2% range
Deadlayer/Active Volume changes

## Slide 6: MCNP Model
25 m radius asteroid[7]
Point source: 100, 10, 1 cm away from surface
Thermal, 0.5, 1, 14.1 MeV, Watt spectrum Neutrons
1, 5, 10, 20 keV X-Rays
+F6 tally (energy dep from all particles) [3]
Total Edep and depth profile tallies
Notes: experiment

## Slide 7: Example Input: SDEF card
Varied: POS, ERG, PAR to test different detonation distances, source particles, particle energies
Watt Spectrum: varying constants did not drastically affect Edep
Notes: Visual, copper lining to prevent X-ray/electron backscatter

## Slide 8: Results
Notes: Sufficient Energy Range

## Slide 9: Results
Notes: Sufficient Energy Range

## Slide 10: Results
Notes: Sufficient Energy Range

## Slide 11: Results
Notes: Sufficient Energy Range

## Slide 12: Conclusion
Edep is highly dependent on particle type and energy.
  Higher source energy = higher Edep
Dependent on isotopic composition of target.
  Function of reaction cross sections of asteroid[6].
Detonation distance and Edep inversely related.
Neutrons more penetrating than hard x-rays

## Slide 13: Future Work
More detailed source term
  Include all types of radiation particles, spectrum for each
Update radiation efficiency calculations
More detailed mesh to tally depth profile radially and across surface
Neutron yield coupling efficiency calculations

## Slide 14: Summary
Problem
Project Goals
Previous Work
MCNP Model
Results
Conclusions

## Slide 15: Acknowledgements
Provided project assistance, Captain James Bevins, AFIT
Provided MCNP template and composition data, MAJ Aaron Ferguson, USA
Michael Bay, Bruce Willis

## Slide 16: References
Github repository
[1] Ferguson, Aaron J. Analysis of Neutron Effects for Asteroid Disruption. 2016. Air Force Institute of Technology. Master’s Thesis.
[2] E. Jarosewich, R. S. Clarke, and J. N. Barrows, ”The Allende meteorite reference sample,” Smithsonian Contributions to the Earth Sciences, vol. 27, p. 49, 1987.
[3] D. B. Pelowitz, ”MCNP6 User’s Manual Version 1.0,” Los Alamos National Laboratory, Los Alamos National Laboratory, 2013.
[4] R. MCCONN, ”Compendium of Material Composition Data for Radiation Transport Modeling,” Pacific North Western National Laboratory, Richland, WA (2011).
[5] S. S. Board et al., Defending Planet Earth:: Near-Earth Object Surveys and Hazard Mitigation Strategies. National Academies Press, 2010.
[6] ”ENDF/B-VII.1 Evaluated Nuclear Data Library.” [Online]. Available: http://www.nndc.bnl.gov/endf/b7.1/
[7] ”NEO Discovery Statistics.” [Online]. Available: http://neo.jpl.nasa.gov/stats/goall
[8] Bodansky, David. Nuclear Energy: Principles, Practices, and Prospects. 2nd ed., Springer, 2005.
[9] Bay, Michael, director. Armageddon. Touchstone Pictures, 1998.

## Slide 17: Questions?
[9]